## Slide 1: Master Control Talk Groups MCT’s Designed by: PNW/DCI Networks Mike Shirley – NO7RF NO7RF@trbo.org
Patrick Stewart – KA6P
Wrightwood, CA
capturecom@gmail.com
21 July 2018

## Slide 2: What are MCTs ?
Special Group Call Talk Groups (TGs)
User commanded TG Control Method
Override default or normal settings & timers
  Most or all TGs on a manager’s Time Slot (TS)
Semi-automatic method to avoid TG “hijacking”
Control TGs on TS 1 and/or TS 2 all via MCTs on TS 1
Not used for voice traffic

## Slide 3: Why MCTs ?
Huge benefit to c-Bridge developers and admins
Eliminates need for individual hold-off timers
  Coding of nn TS hold-off timers for each TG on the TS
    nn = number of TGs on the TS
    Example: 15 TGs in TS requires 15 timers for each of 15 TGs
    225 hold-off timers total need to be coded in this example
MCTs only require 1 timer per TG
Development coding reduced from 6-8 hrs. to 1 hr. for a 15 TG TS
MCT use precludes TG hijacking by network traffic during local use

## Slide 4: How is MCT Controlled?
TGIDs are created for MCT ON and MCT OFF
  Example: Wrightwood DMR Repeater
  MCT ON – TGID 16771811 (All TGs on Both TSs)
  MCT OFF – TGID 16770811 (All TGs on Both TSs)
All MCTs are on TS 1 and can control TGs on either TS
Users enable the functions by kerchunking the appropriate MCT TG

## Slide 5: How Does MCT OFF Work?
User kerchunks MCT “OFF” TG prior to making a call
  C-Bridge turns OFF all TGs programmed for the function
  User kerchunks the TG to be used: it becomes the only active TG
  Selected TG remains protected from network hijacking for 15-29 minutes (c-Bridge programmable)
  MCT OFF time targets average conversation duration
  If activity exceeds the protection time, repeat MCT OFF
  When activity ends, user can kerchunk a common TG
Repeater reverts to normal at end of MCT Timer

## Slide 6: How Does MCT ON Work?
User kerchunks MCT “ON” TG at any time
  Turns ON all TGs programmed for the function
  Can include all Always Active and PTT TGs on all TSs
  Repeater owner can specify ON function configuration
  ON function stays active for 55-59 minutes
User can kerchunk MCT OFF and then select a common TG to be active
Or do nothing and let the MCT ON time out

## Slide 7: What Else?
Local-1 and Local-2 can be programmed to function an MCT OFF command
This uses a shorter duration hold-off time of 5 minutes
Convenient when the user anticipates a short conversation

## Slide 8: MCT Positives
Pro’s:
  Simple for users to understand
  TGs are either ON or they are OFF
  Fewer competing timer interactions to confuse users
  Can easily monitor nets without network contention
  C-Bridge admin time is minimized by a factor of up to 16 times simply to program a new manager
  Local-1 and Local-2 can act as MCT OFF, but shorter duration
  MCT is in-use by many groups: mature and effective

## Slide 9: MCT Negatives
Cons:
  Less intelligent control dynamically during and between conversations
  User should know and remember to initiate MCT OFF before making a call
  May require the use of and space for the additional 1, 2, or 4 more TGs in a Zone (16-CH constraint)
  It is a new approach and sometimes challenging for existing users to adapt

## Slide 10: Summary
Great way to reduce c-Bridge development and maintenance time
Positive and substantial improvement
Users can control how they initiate and maintain TG access (or not)
Proven to work effectively and efficiently with minimal user learning curve
Targeted to c-Bridge developers and admins